## Slide 1
V1 March 2025
A global leader for qualifications, assessment, digital solutions, innovative products and customer service
© 2025 Highfield Products Limited
Highfield Place Shaw Wood Business Park, Shaw Wood Way, Wheatley Hills Doncaster, DN2 5TB
01302 363277 | www.highfieldqualifications.com
All rights reserved
Level 2 Award in Low Airspace Awareness (RQF)
Notes: All rights reserved. No part of this product may be reproduced, stored in a retrieval system, or transmitted in any form or by any means, including electronic, photocopying, recording or other commissioner wise, without the prior permission of Highfield Products Ltd. The of any unauthorised act may result in civil or criminal actions.
The publisher of this product has made every effort to ensure the accuracy of the information contained in this product. However, neither the author, nor Highfield Products Ltd nor anyone involved in the creation of this publication accepts any responsibility for any inaccuracies or failure to implement correctly, however caused.

## Slide 2: Ground rules
Fire escapes
Toilets
Smoking
Drinks
Breaks
Lunch
Questions
Talking over others
Respect others’ points of view
Timekeeping
As a courtesy to others, please set your mobile phone to SILENT MODE
Mobile phones must be SWITCHED OFF and removed from the desk during the examination.
Notes: Introduction
The objective of this section is to outline the content and flow of the course and to introduce course activities and assessment methods.
Suggested total time for introductions to the group and course content etc. is approximately 30 minutes (where a subject related icebreaker is included).
Welcome learners – introduce yourself. Explain domestic arrangements, emergency evacuation procedures, refreshments, security and toilet location.
Ask learners to switch off mobile phones, etc.
Provide a short overview of the course and its purpose.
Encourage participation by asking learners to write their names on badges/stickers or display in front of them.
Refer to the recommended course book and explain the handouts and how they will be used throughout the course.
Discuss how you will use group exercises etc.
It is important that learners are made aware of general housekeeping and safety matters.
This is also an ideal time to establish any ground rules with regards to learners and your own expectations, expected involvement and information regarding home study.
You could also take this opportunity to briefly outline the examination procedures relating to the awarding body being used.
Learners may have received very little information about the course so a short overview will be useful.
The next slides refer to the course materials and how they will be used through the course.

## Slide 3
Module 1: Understand the Drone Code
Module 2: Understand counter-drone technologies and measures to take
Module 3: Understand legal and ethical considerations when encountering drones within low airspaces
Module 4: Understand current and potential threats involving drones and low airspaces.
Learning outcomes

## Slide 4
Module 5: Understand how to complete threat assessments and risk management in relation to drones in low airspaces
Module 6: Understand the practical applications and the continuous development of low airspace security
Module 7: Understand what a drone is and how it works.
Learning outcomes (cont.)

## Slide 5
Understand the
Drone Code
Module 1
5

## Slide 6: Key components of the Drone Code
Before flying a drone, operators must follow the Drone Code to ensure safety, legality and responsible flying
This code outlines essential rules to prevent accidents, respect privacy and comply with airspace regulations, including:
getting what you need to fly legally – operators must register as a drone operator and pass competency tests
flying safely and responsibly – operators must follow safety regulations and conduct risk assessments
where you can fly – it is important that operators understand airspace restrictions and check for no-fly zones.
Notes: Explain how the Drone Code ensures safe and legal UAV operations.
Tutors should consider discussing the following:
250g drones and below need fewer restrictions and do not need to be registered with the Civil Aviation Authority (CAA). Therefore, this gap/loophole will likely be exploited by criminals or nefarious (evil) individuals. Although entirely legal, it may give the security guard an idea of that individual’s intent when operating near sensitive sites.

## Slide 7
making every flight safe – operators should always perform pre-flight checks and assess environmental factors
protecting people’s privacy – operators must respect UK General Data Protection Regulations 2018 (GDPR) on drone footage
less common flying – operators should ensure that they understand special considerations for night flights and commercial operations
drones and model aircraft in the law – operators must know and understand all the legal requirements unmanned aerial vehicle (UAV) pilots must follow.
Key components of the Drone Code (cont.)
Notes: Abbreviations:
visual line of sight (VLOS)
unmanned aerial vehicle (UAV)

## Slide 8: Responsibilities of a UAV operator
To fly safely and legally, drone operators must follow essential regulations to prevent risks, protect privacy and ensure responsible use
The following principles help maintain safety and compliance in all drone operations:
safety of others – avoid endangering people, animals or property
respect for privacy – follow data protection laws when filming or capturing images
awareness of airspace rules – check restricted and controlled airspace zones.
Notes: Explain how operators must follow ethical and legal responsibilities to ensure public safety.

## Slide 9: Responsibilities of a UAV operator (cont.)
maintaining visual line of sight (VLOS) – ensure the drone is always visible to the operator
compliance with altitude limits – stay below the legal height restriction (120m in the UK)
risk assessment and flight planning – consider the weather, obstructions and emergency protocols
accountability and liability – UAV operators are legally responsible for their flights.
Notes: Abbreviations:
visual line of sight (VLOS)
unmanned aerial vehicle (UAV)

## Slide 10: Consequences of ignoring the Drone Code
Failing to follow drone regulations can lead to serious legal, financial and safety consequences
Understanding these risks helps ensure responsible flying and protects both the operator and the public
Risks include:
legal penalties – fines, criminal charges or revocation of flying privileges
financial liability – operators can be held responsible for damages caused by negligence
safety risks – increased chances of mid-air collisions, injuries or accidents.
Notes: Provide real-world examples of UAV-related violations and their consequences.
Tutors should consider discussing the following laws/offences and potential punishments.
For example, causing property damage - Criminal Damage Act 1971 - up to 10 years in prison
Flying a drone while intoxicated - ANO 2016, Article 240 - a fine or up to 2 years in prison
Using a drone for harassment or stalking - Protection from Harassment Act 1997 - up to 5 years in prison
Flying above 400ft or within restricted areas - ANO 2016, Article 94 A -Unlimited fine or up to 5 years in prison if endangering an aircraft

## Slide 11: Understanding low airspace restrictions
Understanding airspace regulations is crucial for safe and legal drone operations
Different restrictions apply depending on location and circumstances, ensuring security and preventing conflicts with other aircraft.
Notes: Discuss how different airspace restrictions impact UAV flight planning.

## Slide 12: Understanding low airspace restrictions (cont.)
Restrictions include:
restricted zones – areas where UAVs are prohibited without special permission
controlled airspace – requires authorisation from air traffic control (ATC)
temporary flight restrictions (TFRs) – enforced during major events, security operations or emergencies
no-fly zones – permanently restricted locations, such as airports, military bases and national security sites
prohibited areas – strictly forbidden due to safety, security or legal reasons.
Notes: Discuss how different airspace restrictions impact UAV flight planning.

## Slide 13: Understanding UAS components
An uncrewed aerial system (UAS) consists of multiple elements working together to ensure safe and effective drone operation
Understanding these components helps operators maintain control, communication and navigation during flight.
Notes: Explain how these 3 key components interact to ensure safe and effective UAV operations.

## Slide 14: Understanding UAS components (cont.)
Components include:
the operator/a ground control system (GCS) – the person controlling the UAV using a remote or autonomous system
the signal between the operator and the drone – the communication link between the operator and the drone, enabling flight control
the drone – the physical aircraft equipped with navigation systems, sensors and cameras.
Notes: Clarify the role of the CAA in governing UAV operations and maintaining safety standards.

## Slide 15: Regulatory authorities of the Drone Code
Regulatory authorities include:
the UK Civil Aviation Authority (CAA) is responsible for enforcing the Drone Code
the CAA ensures compliance with national and international aviation laws
the Drone Code aligns with regulations from the International Civil Aviation Organisation (ICAO)
999 should be called if drones are flying recklessly or being used for criminal activities
101 should be called for non-emergencies, such as illegal drone activity in restricted areas.
Notes: Clarify the role of the CAA in governing UAV operations and maintaining safety standards.

## Slide 16: How much do you know?​
What is the main purpose of the Drone Code?​
CE
To promote drone photography
To limit the use of drones to government agencies
To provide guidelines for safe and legal drone operation
C
C
B
A
Notes: Class exercise
The correct answer is C.

## Slide 17: How much do you know?​
What is a UAV operator responsible for when flying a drone?​
CE
Flying anywhere they choose as long as they are careful
Using the drone only for recreational purposes​
Ensuring compliance with airspace regulations and safety protocols
C
C
B
A
Notes: Class exercise
The correct answer is C.

## Slide 18: How much do you know?​
If a drone is flying recklessly near an airport, what should be done?
CE
Report it to the Civil Aviation Authority (CAA)
Call 999 as it could pose a serious security or safety threat
Ignore it unless it causes damage
B
C
B
A
Notes: Class exercise
The correct answer is B.

## Slide 19
Understand what a drone is and how it works
Module 2
19

## Slide 20: Differences between drone designs
Drones come in many shapes and sizes, each designed for a specific purpose, whether it's a small quadcopter for photography or a fixed-wing drone for long-distance mapping. Understanding the differences is crucial
Drone designs include:
multirotor drones (for example, quadcopters and hexacopters) – highly manoeuvrable, good for stable hovering
fixed-wing drones – longer range, higher speed, but generally requires a runway or launcher
single-rotor drones – more efficient than multirotor drones and is used for heavy lifting
hybrid drones – combine fixed-wing and rotor designs for versatility.
Notes: Ask which type the learner thinks is most useful for deliveries.

## Slide 21: UAS terminology
Drones come with various technical terms such as:
Uncrewed Aircraft System (UAS)
Uncrewed Aerial Vehicle (UAV)
Remotely Piloted Aircraft System (RPAS)
Each refer to different aspects of their operation and control
Understanding these distinctions helps clarify how drones function and are regulated in airspace.
Notes: Discuss why is it important to understand UAS terminology.

## Slide 22: UAS terminology (cont.)
Other terminology may also include:
uncrewed aerial system (UAS) – the complete system, including the drone and ground control
uncrewed aircraft vehicle (UAV) – the drone itself
remotely piloted aircraft system (RPAS) – a drone controlled by an operator
the vehicle – this is the drone
what the drone carries – payload (for example, cameras, sensors and cargo).

## Slide 23: UAS terminology (cont.)
ground control station (GCS) – the operator’s control system
radio frequency (RF) – wireless communication signals
counter-UAS (C-UAS) – technologies used to detect and neutralise drones.

## Slide 24: Drone characteristics
Not all drones are the same. Some fly at high speeds, while others are built for stability
Understanding a drone’s characteristics, such as speed, range and control methods, can help determine its best use case.
Notes: Explain the characteristics that matter most for military drones.

## Slide 25: Drone characteristics (cont.)
Characteristics may include:
speed – varies by design, with fixed-wing being the fastest
range – limited by battery life and signal range
altitude – some drones can reach thousands of feet
control method – manual, semi-autonomous or fully autonomous
sensors – cameras, Light Detection and Ranging (LiDAR), infrared and GPS
payload capacity – determines the drone’s function (for example, delivery or surveillance)
cameras – consumer and commercial drones use cameras for photography, surveillance and mapping. Some are designed for other tasks.
Notes: Tutors to discuss.
The reason why understanding characteristics is so important is because it offers the security guard an idea of what intent the operator has, what the drone is capable of, what it may be used for and what limitations it may have, allowing them to make an informed and well-proportioned judgment and response.

## Slide 26: Positive and negative uses of drones
Drones play a significant role across industries, from delivering life-saving medicine to posing security risks at airports
Their applications range from emergency response and agriculture to surveillance and logistics, while their misuse includes smuggling, hacking and airspace disruption
Understanding these impacts highlights both their potential and the challenges they present.
Notes: Discuss how can drone misuse be controlled.

## Slide 27: Positive and negative uses of drones (cont.)
Positive uses include:
delivery services
surveys
search and rescue
agriculture and environmental monitoring
security and surveillance
emergency services
sporting events
marketing
Negative uses include:
surveillance
smuggling
hacking
attacking
disruption
propaganda
psychological threats
criminal damage.

## Slide 28: How much do you know?​
Which of the following drone designs is most appropriate for hovering and carrying payloads in a stationary position?
CE
Fixed-wing drones ​
Hybrid drones
Multirotor drones
C
C
B
A
Notes: Class exercise
The correct answer is C.

## Slide 29: How much do you know?​
What does ‘payload’ refer to in drone operations?​
CE
The maximum altitude a drone can fly at
The onboard equipment or cargo a drone carries
The amount of fuel a drone consumes
B
C
B
A
Notes: Class exercise
The correct answer is B.

## Slide 30: How much do you know?​
Which of the following is a negative use of drones?​
CE
Surveying land for construction projects
Assisting in search and rescue missions​
Collecting personal data without consent
C
C
B
A
Notes: Class exercise
The correct answer is C.

## Slide 31
Understand counter-drone technologies and measures to take
Module 3
31

## Slide 32: Counter-drone measures
Counter-drone technologies play a crucial role in maintaining security and safety in low airspace
Their importance includes:
protecting sensitive infrastructure – preventing drones from interfering with power plants, government buildings and other critical locations
ensuring public safety – reducing risks to people in crowded areas
preventing airspace disruptions – avoiding interference with commercial and emergency aviation
protecting privacy – stopping unauthorised surveillance or data collection
preventing unauthorised surveillance – countering espionage and other malicious drone activities.
Notes: Explain that counter-unmanned aerial systems (C-UAS) exist to prevent the unauthorised use of drones in sensitive areas. Highlight that this session will cover key counter-drone measures, their technologies, methods of deterrence, strategic elements and impacts. Encourage learners to share their own experiences or concerns about drone security.

## Slide 33: Types of counter-drone technologies
There are various technologies designed to detect and neutralise unauthorised drones, including:
jamming – used to interfere with the communication between a drone and its operator
spoofing – used to deceive a drone’s system by sending false signals to manipulate its behaviour
electronic warfare – the use of electromagnetic signals to detect, disrupt or neutralise unauthorised drones.

## Slide 34: Types of counter-drone technologies (cont.)
kinetic defeat function – counter drone technologies that disable the drone by directly impacting it or its operational capabilities
killer drones – drones that are specifically designed to neutralise or destroy other drones
lasers – direct energy weapons used to disable drones by targeting their critical components
netting – used to physically capture and disable drones by deploying a net
geo-fencing – technology used to establish virtual boundaries, which drones are programmed to recognise and avoid.
Notes: Tutors should explain the following.
Actions a security guard cannot legally take:
shoot down, damage or interfere with a drone – this is criminal damage under UK law
use electronic jamming or hacking – illegal under the Wireless Telegraphy Act 2006
physically capture or net a drone – unless authorised (for example law enforcement or military)
confiscate a drone or equipment – unless it is a direct safety risk to people on private property

## Slide 35: Deterring unauthorised drones
Preventative measures can discourage unauthorised drone activity before intervention is required
Preventative measures include:
signage and warnings – informing operators about no-fly zones
geo-fencing – programming drones to avoid restricted areas automatically
visible security presence – having security personnel monitor drone activity
public awareness campaigns – educating the public on drone regulations
drone registration and licensing – ensuring accountability by making drone operators identifiable.
Notes: Tutor to discuss the following.
Key actions they must take include:
Observe, gather intelligence and identify the drone type (size, speed and behaviour). Look for the operator (they may be within 1-2km for most consumer drones). Note the drone’s features (camera, payload, LED lights and markings). Record timestamps, flight paths and behaviour for evidence.
Report to authorities, for example, the police (101 or 999 in an emergency) if the drone is being used dangerously, for crime or violating airspace laws.

## Slide 36: Key elements of a C-UAS strategy
To effectively counter drone threats, an organised strategy must be in place
Strategies may include:
risk assessment and threat analysis – evaluating the likelihood and impact of drone threats
detection capabilities – using radar, cameras and sensors to identify drones
tracking and identification – determining drone movements and potential risks.

## Slide 37: Key elements of a C-UAS strategy (cont..)
response protocols and procedures – establishing clear steps for intervention
team education and training – ensuring personnel are equipped to handle drone threats
integration with the police – collaborating with law enforcement for enforcement and intelligence-sharing.

## Slide 38: Impacts of counter-drone technologies
The implementation of counter-drone measures has various consequences. These include:
enhanced security – reducing the risks associated with unauthorised drones
public safety – protecting people from drone-related incidents
protection of privacy – preventing unauthorised surveillance and data collection
support for law enforcement – assisting the authorities in handling illegal drone activity
legal and ethical concerns – ensuring countermeasures comply with laws and ethical considerations
collateral damage – potential unintended consequences, such as interference with legitimate drone use
cost implications – investment in counter-drone technology can be expensive but necessary for security.

## Slide 39: How much do you know?​
What is the primary purpose of counter-drone technologies?​
CE
To improve drone battery life
To detect and neutralise unauthorised drones
To increase drone flight range
B
C
B
A
Notes: Class exercise
The correct answer is B.

## Slide 40: How much do you know?​
Which of the following is an example of an active counter-drone measure?​
CE
Public awareness campaigns
Jamming or disabling drones using electronic warfare
Registering drones for accountability
B
C
B
A
Notes: Class exercise
The correct answer is B.

## Slide 41: How much do you know?​
What is a key ethical concern with counter-drone measures?​
CE
Ensuring countermeasures do not interfere with legitimate drone use
Increasing drone surveillance capabilities
Reducing the cost of drone operations
A
C
B
A
Notes: Class exercise
The correct answer is A.

## Slide 42
Understand legal and ethical considerations when encountering drones within low airspaces
Module 4
42

## Slide 43: Legal framework governing drone use
Drone operations in the UK are governed by strict regulations to ensure safety, security and privacy
The main regulations that every drone operator must follow are:
The Drone Code – these are rules set by the Civil Aviation Authority (CAA) for safe drone operation
Air Navigation Order (ANO) – legal regulations defining drone operation in UK airspace
Data Protection Act – governs drone use related to privacy and data collection
No-fly zones – areas restricted for drones, such as airports and military bases
The police – law enforcement authority to confiscate or neutralise illegal drones.
Notes: Discuss what legal consequences might drone misuse lead to.

## Slide 44: Ethical considerations for neutralising drones
Neutralising unauthorised drones requires ethical decision-making. Actions must balance safety, legality and the rights of drone operators
Considerations should be made regarding the following concerns:
safety of bystanders – ensuring no harm to people or property
legal compliance – actions must align with UK laws and regulations
privacy rights – avoiding the misuse of counter-drone measures
justification and proportionality – neutralisation should be a last resort
potential for escalation – ensuring that actions remain proportionate and do not create further risks
impact on legitimate use – preventing disruption of lawful drone operations.
Notes: Explain when it might it be justified to disable a drone.

## Slide 45: Reporting unauthorised or unsafe drone activity
Unauthorised drones can pose security threats. Knowing how to report security threats is crucial for maintaining safe airspace
Before reporting, the following should be considered:
identify the situation – assess if the drone poses a risk
assess the nature of the activity and gather evidence – take photos and videos if safe to do so
contact authorities – report to the police, Civil Aviation Authority (CAA) or air traffic control
provide details – location, time, drone description and any suspicious activity
follow up – ensure authorities are taking action if the drone remains a threat.
Notes: Ask the learner what they should do if they see a drone flying near an airport.

## Slide 46: How much do you know?​
What should you do first when spotting an unauthorised drone in a restricted area?
CE
Attempt to capture the drone yourself
Report it to the appropriate authorities with evidence
Ignore it unless it causes damage
B
C
B
A
Notes: Class exercise
The correct answer is B.

## Slide 47: How much do you know?​
When is neutralising a drone considered ethical?​
CE
When it aligns with legal regulations and poses no harm to bystanders
When someone is annoyed by the drone​
Whenever it enters private property
A
C
B
A
Notes: Class exercise
The correct answer is A.

## Slide 48: How much do you know?​
What is the purpose of the Drone Code in the UK?​
CE
To regulate how drones are manufactured
To prevent all drone flights in urban areas
To provide safety and legal guidelines for drone operators
C
C
B
A
Notes: Class exercise
The correct answer is C.

## Slide 49
Understand current and potential threats involving drones and low airspaces
Module 5
49

## Slide 50: Different threats posed by drones
Drones can be used for many legitimate purposes, but they also pose risks in various environments
Key threats associated with drones in low airspace include:
danger to crewed and uncrewed aircraft – risk of collisions in controlled airspace
stadiums and large crowds – potential for attacks, disruptions or surveillance
airports – unauthorised drones can cause flight delays and safety hazards
contraband delivery to prisons – used for smuggling drugs, weapons or mobile devices.
Notes: Ask learners which of these threats they think is the biggest concern and why.

## Slide 51: Different threats posed by drones (cont.)
surveilling security routines – can be used to map security patterns for illegal activities
corporate espionage – drones may steal trade secrets or conduct unauthorised surveillance
hacking – used to intercept communications or gain access to networks
terrorism – potential tool for targeted attacks or intelligence gathering
delivering a dangerous payload – may carry explosives, hazardous chemicals or biological threats.

## Slide 52: Impact of low airspace threats on safety and security
Drones operating in low airspace can have serious consequences
Threats impact public safety, security and regulations, threats may include:
collision hazards with manned aircraft – risk of mid-air collisions and accidents
threats to public safety – potential for injury or loss of life
compromising security – unauthorised drones can bypass security measures
public anxiety – fear of unknown drone activity in restricted areas
legal and regulatory challenges – difficulty in enforcing drone laws and prosecution
challenges in counter-drone measures – evolving threats require advanced mitigation strategies.
Notes: Discuss the measures that you think can reduce these impacts.

## Slide 53: Signs of unauthorised or suspicious drone activity
Recognising the warning signs of unauthorised drone activity is key to preventing security threats
Indicators that a drone may be operating illegally include:
unfamiliar drone presence – drones appearing in restricted or high-risk areas
erratic flight patterns – sudden movements, changes in direction or hovering
low altitude operations – flying close to buildings, vehicles or people
time of flight – flying at night and trying to conceal lights may provide further evidence towards criminal activity.
Notes: Discuss the actions to take if the learner spots a suspicious drone.

## Slide 54: Signs of unauthorised or suspicious drone activity (cont.)
lack of registration – no visible identification markings or compliance with drone regulations
frequent flyovers – repeated appearances over sensitive areas
unusual payloads – drones carrying objects not typically associated with commercial or hobbyist use
public complaints – reports from concerned citizens or employees noticing unusual drone activity.
Notes: Discuss the actions to take if the learner spots a suspicious drone.

## Slide 55: Future threats of AI-enabled UAS
As artificial intelligence (AI) technology improves, drones are becoming smarter and more autonomous. This presents new security challenges, including:
advanced surveillance – AI drones can conduct real-time tracking and data gathering
precision targeting – improved accuracy for autonomous targeting in security threats
automated attacks – AI drones can be capable of carrying out missions without human input.
Notes: Discuss what the most concerning AI drone threat is and why.

## Slide 56: Future threats of AI-enabled UAS (cont.)
cyberattacks on UAS – AI-controlled drones could be hacked and repurposed
forgery and deception – spoofing drone identities to evade detection
swarm attacks – co-ordinated drone groups used to overwhelm security defences
stealth and evasion – AI systems designed to avoid detection by counter-drone technologies
automated infiltration – AI drones used to penetrate restricted areas without operator control.
Notes: Discuss what the most concerning AI drone threat is and why. Also discuss how the threat environment is changing. For example, while most threats remain low-risk, around 5% could involve drones that are capable of advanced attacks. It is vital that learners can distinguish between autonomous attacks (no human control) and swarm co-ordinated attacks (multiple drones working in sync). Swarm threats, in particular, could pose a major future challenge.

## Slide 57: How much do you know?​
Which of the following is NOT considered a drone-related threat?​
CE
Corporate espionage
Aerial photography for real estate
Smuggling contraband into prisons
B
C
B
A
Notes: Class exercise
The correct answer is B.

## Slide 58: How much do you know?​
What is a sign of suspicious drone activity?​
CE
A drone being flown in a local park during daylight hours
A drone being used for agricultural crop monitoring​
A drone hovering over a restricted area at night
C
C
B
A
Notes: Class exercise
The correct answer is C.

## Slide 59: How much do you know?​
What is a key concern regarding AI-powered drones?​
CE
They can be hacked and repurposed for cyberattacks
They reduce the cost of drone manufacturing
They require more battery power than standard drones
A
C
B
A
Notes: Class exercise
The correct answer is A.

## Slide 60
Understand how to complete threat assessments and risk management in relation to drones in low airspaces
Module 6
60

## Slide 61: Types of passive and active countermeasures
There are 2 types of countermeasures:
Passive – which detect and manage threats
Active – which physically stop drones
Passive countermeasures include:
use of optics for drone detection
recognition of drone threats
tabletop exercises for training
a well-trained workforce
information programmes
the use of a drone to simulate threats.
Notes: Ask why active countermeasures are restricted to certain organisations.

## Slide 62: Types of passive and active countermeasures (cont.)
Active countermeasures include:
jamming – disrupting drone signals
spoofing – sending false signals to mislead drones
shooting – use of a net to capture drones
killer drones – designed to neutralise threats
lasers – used to disable drone components
kinetic defeat functions – physical takedown methods.

## Slide 63: Differences between passive and active countermeasures
Not all countermeasures work the same way. Passive measures help detect threats, while active measures neutralise them
Passive countermeasures:
reduce the threat posed by drones without physically affecting them
do not require approval from governing bodies
are cost-effective
are not always effective, depending on the operators’ intention, such as delivering a payload.
Notes: Discuss which type is more commonly used and why.

## Slide 64: Differences between passive and active countermeasures (cont.)
Active countermeasures:
physically affect unmanned systems or how they operate are reactive solutions.
Notes: Discuss which type is more commonly used and why.

## Slide 65: Legal stipulations of active countermeasures
Because active countermeasures physically disrupt drones, strict legal guidelines apply. These include:
proportionality – any action taken must be justified and necessary
authorisation – only authorised personnel or agencies can deploy active countermeasures
privacy laws – actions must comply with data protection and privacy regulations
liability and accountability – organisations using active countermeasures are legally responsible for their consequences.
Notes: Explain why authorisation is so important for active countermeasures.

## Slide 66: Steps in conducting a threat assessment
Before responding to a drone threat, organisations must assess the risk. A structured threat assessment ensures the right action is taken
The structure should include:
define the scope and objectives of the assessment
identify potential threats from drones
assess the drone’s characteristics and capabilities
analyse the vulnerabilities in security measures
evaluate the likelihood and impact of threats
implement mitigating measures to reduce risk
develop a response plan for security breaches
monitor and review strategies continuously.
Notes: Explain why ongoing monitoring important for drone security.

## Slide 67: Key factors in risk assessment
Several factors influence how drone threats are assessed. Understanding these helps organisations make informed decisions
Factors include the:
type and purpose of drone operations
airspace regulations and restrictions in place
detection and monitoring capabilities
drone capabilities and technological limitations
competency and intent of the drone operator
emergency response preparedness
legal and ethical considerations.
Notes: Discuss the factors that the learner thinks makes a drone more of a security risk.

## Slide 68: How risk assessments inform operational decisions
Once risks are identified, they shape operational decisions.
Risk assessments help organisations decide how to respond to drone threats effectively, such as by:
allocating resources and training personnel effectively
refining response protocols for drone threats
developing incident reporting and escalation procedures
continuous monitoring and adapting to evolving risks
investing in counter-drone technology
informing public safety measures and security policies.
Notes: Ask how can risk assessments improve counter-drone security.

## Slide 69: Organisations permitted to use active countermeasures
Not everyone can legally neutralise drones. Only specific organisations have the authority to use active countermeasures
These organisations include the:
military – national defence organisations can use active countermeasures for security purposes
police – law enforcement agencies can deploy countermeasures to neutralise drone threats in restricted areas.
Notes: Ask why the learner thinks only these organisations are allowed to use active countermeasures.

## Slide 70: How much do you know?​
What is a key legal consideration for using active counter-drone measures?
CE
Ensuring that countermeasures comply with privacy and proportionality laws
Allowing any security personnel to disable drones at will​
Ignoring potential collateral damage when neutralising drones
A
C
B
A
Notes: Class exercise
The correct answer is A.

## Slide 71: How much do you know?​
What is the main difference between passive and active​ countermeasures?
CE
Active measures are cheaper than passive measures
Passive measures always require legal authorisation​
Passive measures detect drones, while active measures physically neutralise them
C
B
A
C
Notes: Class exercise
The correct answer is C.

## Slide 72: How much do you know?​
Who is legally permitted to use active countermeasures against drones?​
CE
The general public if they feel threatened by a drone​
Only the military and police
Any a company with drone detection technology
C
B
A
B
Notes: Class exercise
The correct answer is B.

## Slide 73
Understand the practical applications and the continuous development of low airspace security
Module 7
73

## Slide 74: Ways to practise for a drone incursion
Security teams and operators need to be prepared for potential drone incursions. Various training methods help ensure a quick and effective response
Practise methods include:
simulations and drills – practical exercises to test the response to drone threats
tabletop exercises – discussion-based planning for different incursion scenarios
virtual reality (VR) – immersive training for real-world drone threats
technology familiarisation – understanding counter-drone tools and tracking software
response co-ordination – collaboration between agencies and security teams
legislation reviews – keeping up with legal frameworks for drone security.
Notes: Ask which of these training methods the learner thinks would be most effective for security teams and why.

## Slide 75: Where to seek more information on safe drone use
Drone safety is an evolving field, with new regulations and guidelines introduced regularly
Knowing where to find accurate and up-to-date information is essential for all drone operators
Accurate information can be found using the following resources:
Civil Aviation Authority (CAA) – UK drone regulations and guidance
Drone manufacturers – safety manuals and operational guidelines.
Notes: Explain why it is important for drone users to stay informed about regulations.

## Slide 76: Where to seek more information on safe drone use (cont.)
online learning platforms – courses and certifications in drone operation and security
online resources – drone industry forums, regulatory updates and news
law enforcement – reporting protocols and the legal enforcement of drone regulations.
Notes: Explain why it is important for drone users to stay informed about regulations.

## Slide 77: How to safely secure a drone crash site
A drone crash site can pose multiple risks, including safety hazards, data security concerns and potential evidence loss
Knowing how to secure a crash site properly is essential
Ensure personal and public safety:
  assess the area for hazards
  create a safety perimeter
  use protective equipment if needed.
Notes: Explain the risks associated with handling a crashed drone.

## Slide 78: How to safely secure a drone crash site (cont.)
Protect the drone and surrounding environment:​
    avoid unnecessary movement of the drone​ prevent further damage by isolating the site
  document the scene
  notify relevant authorities
  report the incident to law enforcement or aviation authorities.
    ​

## Slide 79: How to safely secure a drone crash site (cont.)
  Handle the drone safely by:
        disconnecting the power if possible
        containing hazardous materials (for example, damaged batteries)
        minimising handling to preserve forensic evidence
  Manage data retrieval and secure the onboard footage or tracking data
  Prevent unauthorised access to the drone.
    ​

## Slide 80: Key trends in drone usage and technology development
The drone industry is rapidly evolving, with new applications emerging in various sectors
Key trends in drone usage include:
increased commercial applications – logistics, inspections and aerial surveying
growth in public safety and security – drones in law enforcement and emergency response
expansion of consumer and hobbyist markets – increasing personal and recreational drone use.
Notes: Discuss which industries will benefit the most from advancements in drone technology.

## Slide 81: Key trends in drone usage and technology development (cont.)
military and defence applications – surveillance, reconnaissance and tactical deployment
agriculture and environmental monitoring – precision farming and conservation efforts
Advancements in drone technology includes:
advancements in drone technology
enhanced regulatory frameworks
integration with emerging technologies (for example, artificial intelligence (AI), automation and machine learning).
Notes: Discuss which industries will benefit the most from advancements in drone technology.
Tutor to also discuss cyber security and the increased use of drone for last mile delivery as growth areas in the sector.

## Slide 82: Key trends in drone usage and technology development (cont.)
ground control station
increasing use of radio frequency (RF) tracking and communication
development of counter-uncrewed aerial systems (C-UAS)
improved payload capacities for delivery and surveillance
advanced imaging capabilities with high-resolution cameras.

## Slide 83: How much do you know?​
What is a key step when securing a drone crash site?​
CE
Immediately remove the drone from the site
Document the scene and report the incident to authorities
Ignore the drone unless it causes damage
C
B
A
B
Notes: Class exercise
The correct answer is B.

## Slide 84: How much do you know?​
Why is it important to conduct drone incursion training?​
CE
To increase the number of drones in operation
To encourage recreational drone use in restricted airspace​
To improve security teams’ response to unauthorised drone activity
C
B
A
C
Notes: Class exercise
The correct answer is C.

## Slide 85: How much do you know?​
Which of the following is an emerging trend in drone technology?​
CE
Decreasing the use of drones in security operations
Banning all commercial drone applications
Increased integration with AI and automation
C
B
A
C
Notes: Class exercise
The correct answer is C.

## Slide 86
Thank you for listening